ORDINANCE #2020-05C

AN ORDINANCE AMENDING AND SUPPLEMENTING Chapter 74, “Construction Codes Uniform,” of the Borough Code of the Borough of Beach Haven, County of Ocean, State of New Jersey to include regulations for bulkhead installation.

PURPOSE

The purpose of this Ordinance is to amend Chapter 74 of the Borough Code to add regulations for bulkhead installation.

NOW THEREFORE, THE MAYOR AND COUNCIL OF THE BOROUGH OF BEACH HAVEN DO ORDAIN:

SECTION I

Section 74-30, “Bulkheads,” be and is hereby created, which shall read as follows:

#### § 74-30. Bulkheads.

A. Permit required. Before any work of the type described in this section may begin, the property shall apply for and obtain a building permit after submission of plans and specifications showing compliance with the provisions hereof.  Any work in progress shall be subject to inspection by the Construction Official or Building Inspector to ensure compliance therewith.

B. Construction specifications bayside and lagoon bulkheads. The following requirements shall apply, as applicable:

(1) All sheathing shall be of sufficient length to have the amount buried below the bay bottom equal to the amount exposed above the bay bottom.

(2) Whalers shall be not less than six by six (6 x 6) inches, of which there shall be two.

(3) All pilings shall have eight-inch minimum diameter butts and shall penetrate 10 feet below bay bottom and be five feet on center maximum.

(4) All tie-rods shall not be less than 3/4 inch diameter and 16 feet in length and shall be set through each piling one foot from the top. All anchor pilings shall not be less than 12 feet in length and shall have eight-inch minimum diameter butts.  All tie-rods, bolts and other hardware shall be hot-dipped galvanized.

(5) The top of any bulkhead shall have an elevation of five feet above mean sea level, NAVD 1988.

(6)  All materials shall have a wood

preservative treatment of 2.5- pounds per

cubic foot- CCA.

SECTION II

All Ordinances or parts of Ordinances inconsistent herewith are repealed to the extent of such inconsistency.  The Clerk of the Borough is authorized to renumber and/or re-codify any sections affected by such repeal to the extent consistent with this Ordinance.

SECTION III

If any word, phrase, clause, sections, or provision of this Ordinance shall be found by any Court of competent jurisdiction to be unenforceable, illegal, or unconstitutional, such word, phrase, clause, section, or provision shall be severable from the balance of the Ordinance and the remainder of the Ordinance shall remain in full force and effect.

SECTION IV

This Ordinance shall take effect upon publication thereof after final passage according to law.

NOTICE

Public Notice is hereby given that the foregoing Ordinance was introduced and passed on the first reading at a public meeting of the Borough Council of the Borough of Beach Haven, County of Ocean, State of New Jersey, held on March 9, 2020 at 6:00 p.m.  A copy of the ordinance can be obtained, without cost, by any member of the general public at the Office of the Municipal Clerk, 300 Engleside Avenue, Beach Haven, NJ 08008 Monday through Friday, 9:00 a.m. to 4:00 p.m.

# Further public notice is hereby given that said ordinance shall be considered for final passage and adoption at a public meeting of the Borough Council to be held on April 13, 2020 at 6:00 p.m. at the Beach Haven Municipal Building, 300 Engleside Avenue, Beach Haven, New Jersey 08008.

CERTIFICATION

I, Sherry Mason, RMC, Municipal Clerk of the Borough of Beach Haven, do hereby certify that the foregoing Ordinance was duly adopted by the Borough Council of the Borough of Beach Haven at a regular meeting held on the 9th day of March, 2020, a quorum being present and voting in the majority.

IN WITNESS WHEREOF, I have hereunto set my hand an official seal this 9th day of March, 2020.

_________________

Sherry Mason, RMC, Municipal Clerk

First Reading:	March 9, 2020

First Publication:	March 19, 2020

Second Reading:	April 13, 2020

Second Publication:	April 23, 2020

Final Adoption:	May 3, 2020